## Slide 1: 1.206J/16.77J/ESD.215J Airline Schedule Planning
Cynthia Barnhart
Spring 2003

## Slide 2: 1.963/1.206J/16.77J/ESD.215J The Schedule Design Problem
Outline
  Problem Definition and Objective
  Schedule Design with Constant Market Share
  Schedule Design with Variable Market Share
  Schedule Design Solution Algorithm
  Results
  Next Steps
  A Look to the Future in Airline Schedule Optimization

## Slide 3: Airline Schedule Planning
Assign aircraft types to flight legs
such that contribution is maximized
Schedule Design
Fleet Assignment
Aircraft Routing
Crew Scheduling
Select optimal set of flight legs
in a schedule
Notes: I will now present an overview of the airline schedule planning process. It begins with schedule design, in which… Next is fleet assignment, in which…. 3rd is aircraft routing, in which…. And the last is crew scheduling, in which…. We will now move to our 2nd section, our 1st look at the fleet assignment problem.

## Slide 4: Objectives
Given origin-destination demands and fares, fleet composition and size, fleet operating characteristics and costs
Find the revenue maximizing flight schedule

## Slide 5: Schedule Design: Fixed Flight Network, Flexible Schedule Approach
Fleet assignment model with time windows
  Allows flights to be re-timed slightly (plus/ minus 10 minutes) to allow for improved utilization of aircraft and improved capacity assignments
Initial step in integrating flight schedule design and fleet assignment decisions

## Slide 6: Schedule Design: Optional Flights, Flexible Schedule Approach
Fleet assignment with “optional” flight legs
  Additional flight legs representing varying flight departure times
  Additional flight legs representing new flights
  Option to eliminate existing flights from future flight network
Incremental Schedule Design

## Slide 7: Integrated, Incremental Schedule Design and Fleet Assignment Models
Addition Candidates
Mandatory Flight List
Deletion Candidates
Base Schedule
Optional Flight List
Master Flight List
Select optimal set of flight legs from master flight list
Assign fleet types to flight legs
Notes: We are moving to the 3rd section, schedule design. Our approach to the schedule design problem is incremental.
This is the approach similar to the state of the practice. The only difference is that we use model to select flights while airlines use human to select flights.

## Slide 8: Demand and Supply Interactions
A
B
Market Share
450
A
B
100
150
100
100
Market Share
410
A
B
Market Share
300
100
200
40
100
190
120
150
Non-Linear
Interactions

## Slide 9: Schedule Design: Constant Market Share Model
Constant market share model
  Integrated Schedule Design and Fleet Assignment Model (ISD-FAM)
  Utilize recapture mechanism to adjust demand approximately
Notes: We develop 2 models based on IFAM, namely,…

## Slide 10: ISD-FAM: Example
A
B
Market Share
450
100
150
100
100
Market Share
450
100
150
100
100
A
B
100 + recap1
150 + recap2
100 + recap3
A
B

## Slide 11: ISD-FAM Formulation
Notes: Here is the formulation

## Slide 12: ISD-FAM Formulation
Flight Selection
FAM
PMM
Notes: Here is the formulation

## Slide 13: ISD-FAM Formulation
Flight Selection
FAM
PMM
Fleet Assignment
Spill + Recapture
Schedule Design
Notes: Here is the formulation

## Slide 14: Schedule Design: Variable Market Share Model
Variable market share model
  Extended Schedule Design and Fleet Assignment Model (ESD-FAM)
  Utilize demand correction term to adjust demand explicitly
Notes: We develop 2 models based on IFAM, namely,…

## Slide 15: ESD-FAM: Demand Correction
Demand Correction Terms
A
B
Market Share
450
100
150
100
100
A
B
100
150+40+40
A
B
Market Share
410
40
100
190
120
100 + 0
150 + 40
100 + 20
80
150
-30
2nd degree
correction
Data Quality Issue

## Slide 16: ESD-FAM Formulation

## Slide 17: ESD-FAM Formulation
ISD-FAM
Market Share Adjustment

## Slide 18: ESD-FAM Formulation
ISD-FAM
Market Share Adjustment
Constant
Market Share
Schedule Design
& Fleet Assgn.
Market Share Adjustment

## Slide 19: Solution Algorithm
START
Calculate new demand
for the resulting schedule
Update modifiers
STOP
YES
Identify itineraries that
cause discrepancies
NO
Has the
stopping criteria
been met?
Solve I/ESD-FAM
Contribution 1
Obtain revenue estimates
from PMM
Contribution 2
Notes: We employ an iterative solution algorithm. The algorithm works as follows.

## Slide 20: State Of The Practice/ Theory
Practice:
Most schedule decisions made without optimization
At least one major airline uses Fleet Assignment with Time Windows
Implementation of Incremental Schedule Design approach underway at a major airline
Theory:
Models and algorithms for incremental schedule design have been developed and prototyped
Validation in progress

## Slide 21: Computational Experiences
ISD-FAM requires long runtimes and large amounts of memory
  ~ 40 minutes on a workstation class computer for medium size (800 legs) schedules
  ~ 20 hours on a 6-processor workstation, running parallel CPLEX for full size (2,000 legs) schedules
ESD-FAM takes even longer runtimes and exhausts the memory in some cases
  40 mins (ISD-FAM) vs. 12 hrs (ESD-FAM) on same medium size schedule
Notes: We implement our model

## Slide 22: Schedule Design: Results
Demand and supply interactions
  ESD-FAM captures interactions more accurately
Resulting schedules operate fewer flights
  Lower operating costs
  Fewer aircraft required
~$100 - $350 million improvement annually
  Compared to planners’ schedules
  Exclude benefits from saved aircraft

## Slide 23: Schedule Design Results
Results are subject to several caveats
  Plans are often disrupted
  Competitors’ responses
  Underlying assumptions
    Deterministic demand
    Optimal control of passengers
    Demand forecast
    Recapture rates/Demand correction terms
Nonetheless, significant improvements are achievable

## Slide 24: Potential for Improved Results
Replace IFAM with SFAM
1

## Slide 25: SFAM Basic Concept
Isolate network effects
  Spill occurs only on constrained legs
Potentially
Constrained
Flight Leg
Unconstrained
Flight Leg
Potentially
Binding
Itinerary
Non
-
Binding
Itinerary
Potentially
Constrained
Flight Leg
Unconstrained
Flight Leg
Potentially
Binding
Itinerary
Non
-
Binding
Itinerary
FAM
IFAM


















SFAM

## Slide 26: A Look to the Future: Airline Schedule Planning Integration
Schedule Design
Fleet Assignment
Aircraft Routing
Crew Scheduling
Schedule Design
Fleet Assignment
Fleet Assignment
Aircraft Routing
Aircraft Routing
Crew Scheduling
Fleet Assignment
Crew Scheduling
Integrating crew scheduling and fleet assignment models yields:
Additional 3% savings in total operating, spill and crew costs
  Fleeting costs increase by about 1%
  Crew costs decrease by about 7%

## Slide 27: A Look to the Future: Real-time Decision Making
For a typical airline, about 10% of scheduled revenue flights are affected by irregularities (like inclement weather, maintenance problems, etc.)
According to the New York Times, irregular operations (due mostly to weather) result in more than $440 million per year in lost revenue, crew overtime pay, and passenger hospitality costs
Increasing use and acceptance of optimization-based decision support tools for operations recovery

## Slide 28: A Look to the Future: Robust Scheduling
Issue: Optimizing “plans” results in minimized planned costs, not realized costs
  Optimized plans have little slack, resulting in
    Increased likelihood of plan “breakage” during operations
    Fewer recovery options
Challenge: Building “robust” plans that achieve minimal realized costs