## Slide 1: 1.206J/16.77J/ESD.215J Airline Schedule Planning
Cynthia Barnhart
Spring 2003

## Slide 2: 1.206J/16.77J/ESD.215J Airline Schedule Planning
Outline
  Sign-up Sheet
  Syllabus
  The Schedule Planning Process
  Flight Networks
    Time-line networks
    Connection networks
  Acyclic Networks
  Shortest Paths on Acyclic Networks
  Multi-label Shortest Paths on Acyclic Networks

## Slide 3
Fleet Planning
Schedule
Planning
-
Route Development
-
Schedule Development
o
Frequency Planning
o
Timetable Development
o
Fleet Assignment
o
Aircraft Rotations
Crew Scheduling
Airport Resource
Management
Pricing
Revenue
Management
Sales and
Distribution
Operations Control
SHORT TERM
LONG TERM
TACTICAL
STRATEGIC
Time Horizon
Types of Decision

## Slide 4: Airline Schedule Planning
Route individual aircraft honoring
maintenance restrictions
Assign aircraft types to flight legs
such that contribution is maximized
A flight specifies origin, destination,
and departure time
Contribution = Revenue - Costs
Schedule Design
Fleet Assignment
Aircraft Routing
Crew Scheduling
Select optimal set of flight legs
in a schedule
Assign crew (pilots and/or flight
attendants) to flight legs
Notes: I will now present an overview of the airline schedule planning process. It begins with schedule design, in which… Next is fleet assignment, in which…. 3rd is aircraft routing, in which…. And the last is crew scheduling, in which…. We will now move to our 2nd section, our 1st look at the fleet assignment problem.

## Slide 5: Airline Schedule Planning: Integration
Schedule Design
Fleet Assignment
Aircraft Routing
Crew Scheduling

## Slide 6: Airline Schedule Planning: Integration
Schedule Design
Fleet Assignment
Aircraft Routing
Crew Scheduling

## Slide 7: Flight Schedule
Minimum turn times = 30 minutes
Flight No. | Origin | Destin. | Dep. Time | Arrival Time
1 | A | B | 6:30 | 8:30
2 | B | C | 9:30 | 11:00
3 | C | B | 16:00 | 17:00
4 | B | A | 18:00 | 20:00

## Slide 8: Time-Space Flight Network Nodes
Associated with each node j is a location l(j) and a time t(j)
A Departure Node j corresponds to a flight departure from location l(j) at time t(j)
An Arrival Node j corresponds to a flight arrival at location l(j) at time t(j) – min_turn_time
  t(j)= arrival time of flight + min_turn_time = flight ready time
Notes: <number>
<date/time>

## Slide 9: Time-Space Flight Network Arcs
Associated with each arc jk (with endnodes j and k) is an aircraft movement in space and time
A Flight Arc jk represents a flight departing location l(j) at time t(j) and arriving at location l(k) at time t(k) – min_turn_time
A Ground Arc or Connection Arc jk represents an aircraft on the ground at location l(j) (= l(k)) from time t(j) until time t(k)
Notes: <number>
<date/time>

## Slide 10: Time-Line Network
8:00
12:00
16:00
20:00
8:00
12:00
16:00
20:00
City A
City B
City C
City D
Ground arcs

## Slide 11: Connection Network
8:00
12:00
16:00
20:00
8:00
12:00
16:00
20:00
City A
City B
City C
City D
Connection arcs

## Slide 12: Time-Line vs. Connection Flight Networks
For large-scale problems, time-line network has fewer ground arcs than connection arcs in the connection network
  Further reduction in network size possible through “node consolidation”
Connection network allows more complex relations among flights
  Allows a flight to connect with only a subset of later flights

## Slide 13: Time-Line Network
I
J
A
C
F
H
D
E
B
G

## Slide 14: Node Consolidation
I
J
A
C
F
H
D
E
B
G

## Slide 15: Flight Networks and Shortest Paths
Shortest paths on flight networks correspond to:
  Minimum cost itineraries for passengers
  Maximum profit aircraft routes
  Minimum cost crew work schedules (on crew-feasible paths only)
Important to be able to determine shortest paths in flight networks

## Slide 16: Shortest Path Challenges in Flight Networks
Flight networks are large
  Thousands of flight arcs and ground arcs; thousands of flight arcs and tens of thousands connection arcs
For many airline optimization problems, repeatedly must find shortest paths
Must consider only “feasible” paths when determining shortest path
  “Ready time” (not “arrival time”) of flight arrival nodes ensures feasibility of aircraft routes
  Feasible crew work schedules correspond to a small subset of possible network paths
    Identify the shortest “feasible” paths (i.e., feasible work schedules) using multi-label shortest path algorithms

## Slide 17: Acyclic Directed Networks
Cyclic Networks
Acyclic Networks
Time-line and Connection networks are acyclic directed networks

## Slide 18: Acyclic Networks and Shortest Paths
Efficient algorithms exist for finding shortest paths on acyclic networks
  Amount of work is directly proportional to the number of arcs in the network
  Topological ordering necessary
    Consider a network node j and let n(j) denote its number
    The nodes of a network G are topologically ordered if for each arc jk in G, n(j) < n(k)

## Slide 19: Topological Orderings
1
2
3
6
5
4
1
2
3
4
5
6
7
1
3
7
6
5
4
2
1
5
7
6
4
3
2
X
X
X
X
X
X
X
X
X
X
X
Notes: CB TO DO: Next time do algorithm on its own slide– see Amy’s topo ordering slide from textbook work

## Slide 20: Topological Ordering Algorithm
Given an acyclic graph G, let n= 1 and n(j)=0 for each node j in G
Repeat until n=|N|+1 (where |N| is the number of nodes in G)
  Select any node j with no incoming arcs and n(j) = 0.
  Let n(j) = n
  Delete all arcs outgoing from j
  Let n = n+1

## Slide 21: Shortest Paths on Acyclic Networks
1
2
3
4
5
6
7
8
9
10
(10)
(0)
(1)
(1)
(1)
(1)
(0)
(0)
(0)
(1)
(0)
(0)
(1)
(1)
(1)
1: inf, -1
n(j): l(j), p(j)
2: inf, -1
3: inf, -1
4: inf, -1
5: inf, -1
6: inf, -1
7: inf, -1
8: inf, -1
9: inf, -1
10: inf, -1
1: 0, 0
2: 10, 1
3: 0, 1
8: 10, 2
5: 11, 2
5: 0, 3
4: 1, 3
8: 2, 4
6: 1, 4
7: 1, 5
6: 1, 5
7: 1, 5
9: 1, 6
10: 1, 7
9: 1, 6
10: 1, 7

## Slide 22: Shortest Path Algorithm for Acyclic Networks
Given acyclic graph G, let l(j) denote the length of the shortest path to node j, p(j) denote the predecessor node of j on the shortest path and c(jk) the cost of arc jk
Set l(j)=infinity and p(j)= -1 for each node j in G, let n=1, and set l(1)= 0 and p(1)=0
For n<|N|+1
  Select node j with n(j) = n
  For each arc jk let l(k)=min(l(k), l(j)+c(jk))
    If l(k)=l(j)+c(jk), set p(k)=j
  Let n = n+1

## Slide 23: Multiple Label (Constrained) Shortest Paths on Acyclic Networks
Consider the objective of finding the minimum cost path with flying time less than a specified value F
Let label tp(j) denote the flying time on path p to node j and label lp(j) denote the cost of path p to node j, for any j
Only paths with tp(j) < F, at any node j, are considered (the rest are excluded)
A label set must be maintained at node j for each non-dominated path to j
  A path p’ is dominated by path p at node j if lp’(j) > lp(j) and tp’(j) > tp(j)
  If p’ is not dominated by any path p at node j, p’ is non-dominated at j
  In the worst case, a label set is maintained at each node j for each path p into j

## Slide 24: Constrained Shortest Paths and Crew Scheduling
Label sets are used to ensure that the shortest path is a “feasible” path
  Labels are used to count the number of work hours in a day, the number of hours a crew is away from their home base, the number of flights in a given day, the number of hours rest in a 24 hour period, etc…
  In some applications, there are over 2 dozen labels in a label set
Many paths are non-dominated
Exponential growth in the number of label sets (one set for each non-dominated path) at each node

## Slide 25: Shortest Paths on Acyclic Networks
1
2
3
4
5
6
7
8
9
10
(10, 0)
(0,0)
(1, 2)
(1, 1)
(1, 5)
(1, 1)
(0, 3)
(0, 2)
(0, 4)
(1, 2)
(0, 1)
(0, 1)
(1, 1)
(1, 2)
(1, 3)
1: inf, inf, -1, -1
p: lp1(j), lp2(j), pp(j), ppp(j)
1: inf, inf, -1, -1
1: inf, inf, -1, -1
1: inf, inf, -1, -1
1: inf, inf, -1, -1
1: inf, inf, -1, -1
1: inf, inf, -1, -1
1: inf, inf, -1, -1
1: inf, inf, -1, -1
1: inf, inf, -1, -1
1: 0, 0, 0, 0
1: 10, 0, 1, 1
1: 0, 0, 1, 1
1: 10, 1, 2, 1
1: 11, 1, 2, 1
1: 0, 1, 3, 1
1: 1, 1, 3, 1
2: 2, 3, 4, 1
1: 1, 3, 4, 1
1: 1, 3, 5, 1
1: 1, 3, 5, 1
1: 1, 3, 5, 1
1: 1, 6, 6, 1
1: 1, 7, 7, 1
2: 2, 4, 7, 1
2: 11, 6, 8, 1
3: 3, 8, 8, 2
Max value of label 2 = 7
Infeasible
Dominated

## Slide 26: Constrained Shortest Path Notation for Acyclic Networks
Given acyclic graph G,
  lpk(j) denotes the value of label k (e.g., length, flying time, etc.) on label set p at node j
  pp(j) denotes the predecessor node for label set p at node j
  ppp(j) denotes the predecessor label set for label set p at node j
  c(jk) denotes the cost of arc jk
  m denotes the maximum possible number of non-dominated label sets at any node j
  np(j) denotes the number of non-dominated label sets for node j

## Slide 27: Constrained Shortest Path Algorithm for Acyclic Networks
For p = 1 to m, let lpk(j)=infinity for each k, and np(j)=0, pp(j)= -1 and ppp(j)= -1 for each node j in G
Let n=1 and set np(1)=1, l1k(1)= 0 for each k, p1(1)=0 and pp1(1)=0
For n<|N|+1
  Select node i with n(i) = n
  For each non-dominated p at node i
    For each arc ij, let np(j)= np(j)+1, pnp(j)(j)=i, ppnp(j)(j)=p
      For each k, let lnp(j)k(j) =lpk(i)+c(ij)
    If lnp(j)k(j)>lsk(j) for some s=1,..,np(j)-1, then dominated and set np(j)= np(j)-1
  Let n = n+1